## Slide 1: Aquifer Storage Recharge
Justin & David

## Slide 2: Situation
20m
10<Kh<50 [m/d]
Salt = 30g/l
40 000 m^3 in August & July

## Slide 3: Time planning
Divided work that needs to be done | Amount of time need to put in per person | Finished before | Planned working days
Literature search | 16 hours | 22/Dec | 20 and 21 December
Design ASR system | 16 hours | 10/Jan | 08/Jan
Producing schedule for injection, extraction and storage | 8 hours | 11/Jan | 10/Jan
Reduce waste of injected drinking water | 8 hours | 18/Jan | 12/Jan
Apply guidelines for injection pressure and maximum velocity | 8 hours | 22/Jan | 18/Jan
Run model for 10 years with a start-up year and less extracted volume | 8 hours | 24/Jan | 22/Jan
Making conclusion and finish report | 8 hours | 25/Jan | 24/Jan

## Slide 4: Literature search
Comparable systems
  Good practice
  Idea of feasibility
  Rules of thumb
Choose location?
Get guidelines for injection pressure

## Slide 5: Maximum infiltration rate
Follows from maximum infiltration pressure:
          (De Glee)
      k = hydraulic conducitivity of aquifer (m/d)
      D = thickness of aquifer (m)
      c = hydraulic resistance of confining layer (d)
      rwell = well radius (m)
      hin = infiltration head (m + land surface)
      h0 = natural hydraulic head in aquifer (m + land surface)
In practice: decreases due to gradual well clogging
Infiltration
Van Dooren et al. (2020): https://library.kwrwater.nl/publication/61802381/
hin
h0

## Slide 6: Particle mobilization
Maximum allowed specific discharge on the borehole (qmax in m/s)
(Huisman, empirical)
      L = screen length (m)
      rwell = well radius (m)
      k = hydraulic conductivity (in m/s)
      Van der Schans & Meerkerk (2019): https://library.kwrwater.nl/publication/60518580/
      Olsthoorn (1976): https://edepot.wur.nl/403280
Extraction

## Slide 7: Soil compaction ‘zetting’ (in Dutch)
Drawdown = lowering of pore pressure
Koppejan:
      Z = soil compaction (m)
      d = thickness of confining layer (m)
      Cp = primary compaction constant (-)
      Cs = secular compaction constant (-)
      Φ = pore pressure (kN/m2)
      dΦ = change of pore pressure (kN/m2)
      t = time (days)
Extraction
Drijver (2002): https://edepot.wur.nl/358642
http://www.grondwaterformules.nl/index.php/formules/onttrekking/deklaag-zonder-rand-de-glee

## Slide 8: Design ASR system
MODFLOW6 model
  Adjust parameters
  Background flow?
Optimise model to reduce waste
Ensure guidelines for injection pressure and maximum velocity are met
Run model for 10 years with a start-up year and less extracted volume

## Slide 9: Producing schedule for injection, extraction and storage
Injection
  Analysis of when water excess
Extraction
  Water deficit – July & august:
    Schedule for 1 year & 10 years
Storage possibly above ground if pumping rate too low

## Slide 10: Report
Discuss the uncertainties in your design.
  Changes in Kh
    Scenarios?
Present findings